## Slide 1: 7.4.5 Real Time Conferencing

## Slide 2: Voice Over IP or Internet Telephony
Voice-over-IP is a very popular system, due to its economic benefits. In short, it’s cheap. It allows companies to use the networks already in place rather than having to set up new telephone lines.
Pehr Anderson was the pioneer behind Voice-over-IP. He and his group of friends turned in a similar system for a class project and received a B. Not to be deterred, Pehr started the company NBX in 1996 and sold it for 90 million in 1999.

## Slide 3: How has Voice-Over-IP translated into the systems we have today?
Voice-over-IP being connected to computers started when computer systems started being created with the microphones, cameras, and speakers to be able to support and process media.
A popular example of an early conferencing system was Skype, a system that led to the creation of things we use today such as Zoom for our online classes or discord, for communicating with friends.
As network bandwidth kept improving, video calls began to gain popularity alongside voice calls.

## Slide 4: How does Real Time Conferencing work?
For us, anytime our voice calls or video calls begin to break up or buffer, the common blame falls to our internet service. However, the requirements for maintaining two way conversation is much more difficult than streaming a service or watching a live event. The main difference is the required low latency.
The highest latency that was passable by customers before it became an annoyance was 150 msec.
Due to the required low latency connection requirement, the proper system to use is UDP rather than TCP due to TCPs retransmissions creating delay.

## Slide 5: Limits of Video Conferencing
Not all forms of latency can be reduced. The distance between Seattle and Amsterdam is 8000 km. The propagation delay of the speed of light for that distance is 40 msec. Obviously, in practice, the delay will never be that low.
Video conferencing cannot use large packets due to the latency required for one to process. A 1-KB packet takes 125 msec to fill, and can be longer if samples are compressed and will take at least 8 msecs to transmit the package over a link that runs at 1 Mbps.
Obviously, large packets are a no go, so Voice-over-IP systems use short packets to reduce latency even with the lower bandwidth efficiency.

## Slide 6: Limits of Video Conferencing Continued
Software overhead can also eat up delay budget and cause unacceptable conferencing. Because we are not streaming, the encoder can not compress the file. Therefore, both the encoder and decoder must run quickly.
When a packet takes too long to arrive, the video player will hide the loss but repeating frames or hiding audio behind ambient sound.
Network Layers however can reduce latency, or at least jitter, by utilizing “quality of service” mechanisms. The only time latency is unimportant in real time conferencing is when you have enough network bandwidth for everyone which is not a realistic case.

## Slide 7: Question What grade did Pehr Anderson get on his prototype of Voice-Over-Ip?

## Slide 8: Citations
All information was retrieved from the textbook.