## Slide 1: Self-Healing Control Flow Protection in Sensor Applications

## Slide 2
Motivation
  Sensors usually have very tight resources and use very simple OS and application software
  Data/System memory are not separated
  System/User tasks are not isolated
  No recovery scheme: crash and reboot
  Cannot embed complicated protection methods into the system
  Still need to protect the memory/OS image

## Slide 3
Approach from 500 miles away
  Divide the program into blocks and generate control flow graph
  Assign a different label to each program block. When transitions among blocks happen, examine the labels to make sure such transitions are legal
  If not, remove the task and take back the resources to clean it up

## Slide 4
Overview of the program structure

## Slide 5: Details of the design
Divide programs into blocks
  Every function is a Control Node
  Can detect only illegal transitions among functions

## Slide 6
How to detect illegal transitions
  Each CN is assigned with a label value
  When we enter the function, Rx = label
  When we leave the function, we check again whether or not the label ?= Rx
    If attackers have control the program and jump into another function, the label will have a different value

## Slide 7
New problem: how to protect the label value
  At the compilation time, inject randomness so that every sensor has different access control code segments
  The labels are in write-protected program memory
  What is the label anyway:
    A 8-bit or 16-bit random number

## Slide 8
How to recovery
  Sensor OS can handle only one task at a time
  Therefore, just kill that task and get back all the resources will be fine
  Not as simple as this when we consider the memory management scheme

## Slide 10
Now we have separated kernel memory and task memory
During recovery
  Release the task related memory
  Release the I/O resources
  Remove the current task from the task queue
  Fetch the next task

## Slide 11
Discussion
  Where do we put the label
    Rx can be in registers or memory space
    But where do we put the label of each function?